## Slide 1: Telecommunications and Networking
Note: these are slides that were part of a CISSP prep course that I partly developed and taught while I was with Ernst and Young.
While these slides are dated – August 1999 - the core information is still relevant.
Contact me w/ any questions or comments –
Ben Rothke, CISSP brothke@hotmail.com

## Slide 2: Objective
Upon completion of this lesson, you will:
Explain and understand the OSI model
Identify network hardware
Understand LAN topologies
Know basic protocols - routing and routed
Understand IP addressing scheme
Understand subnet masking
Understand basic firewall architectures
Understand basic telecommunications security issues

## Slide 3: Course Outline
Intro to OSI model
LAN topologies
OSI revisited
  hardware
  bridging,routing
  routed protocols, WANs
IP addressing, subnet masks
Routing Protocols

## Slide 4: OSI/ISO ??
OSI model developed by ISO, International Standards Organization
IEEE - Institute of Electrical and Electronics Engineers
NSA - National Security Agency
NIST - National Institute for Standards and Technology
ANSI - American National Standards Institute
CCITT - International Telegraph and Telephone Consultative Committee

## Slide 5
OSI Reference Model
Open Systems Interconnection Reference Model
  Standard model for network communications
  Allows dissimilar networks to communicate
  Defines 7 protocol layers (a.k.a. protocol stack)
  Each layer on one workstation communicates with its respective layer on another workstation using protocols (i.e. agreed-upon communication formats)
  “Mapping” each protocol to the model is useful for comparing protocols.

## Slide 6
OSI MODEL DIAGRAM
Provides data representation between systems
Establishes, maintains, manages sessions
example - synchronization of data flow
Provides end-to-end data transmission integrity
Switches and routes information units
Provides transfer of units of information to other end of physical link
Transmits bit stream on physical medium
6
5
4
3
2
1
Provides specific services for applications such as
file transfer
7
Application
Presentation
Session
Transport
Network
Data Link
Physical
Developed by the International Standards Organization
Mnemonic: All People Seem To Need Data Processing
Notes: 6

## Slide 7
OSI Reference Model Data Flow
6
5
4
3
2
1
7
Application
Presentation
Session
Transport
Network
Data Link
Physical
CLIENT
SERVER
Data travels down the stack
Through the network
Then up the receiving stack
6
5
4
3
2
1
7
Application
Presentation
Session
Transport
Network
Data Link
Physical
As the data passes through each layer on the client information about that layer is added to the data.. This information is stripped off by the corresponding layer on the server.

## Slide 8: OSI Model
Everything networked is covered by OSI model
Keep model in mind for rest of course
All layers to be explored in more detail

## Slide 9: SECTION
LAN TOPOLOGIES
  Physical Layer
EXAMPLE TYPES

## Slide 10: LAN Topologies
Star
Bus
Tree
Ring

## Slide 11: Star Topology
Telephone wiring is one common example
  Center of star is the wire closet
Star Topology easily maintainable

## Slide 12: Bus Topology
Basically a cable that attaches many devices
Can be a “daisy chain” configuration
Computer I/O bus is example

## Slide 13: Tree Topology
Can be extension of bus and star topologies
Tree has no closed loops

## Slide 14: Ring Topology
Continuous closed path between devices
A logical ring is usually a physical star
Don’t confuse logical and physical topology
MAU

## Slide 15: Network topologies

## Slide 16: LAN Access Methods
Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
  Talk when no one else is talking
Token
  Talk when you have the token
Slotted
  Similar to token, talk in free “slots”

## Slide 17: LAN Signaling Types
Baseband
  Digital signal, serial bit stream
Broadband
  Analog signal
  Cable TV technology

## Slide 18: LAN Topologies
Ethernet
Token Bus
Token Ring
FDDI

## Slide 19: Ethernet
Bus topology
CSMA/CD
Baseband
Most common network type
IEEE 802.3
Broadcast technology - transmission stops at terminators

## Slide 20: Token Bus
IEEE 802.4
Very large scale, expensive
Usually seen in factory automation
Used when one needs:
  Multichannel capabilities of a broadband LAN
  resistance to electrical interference

## Slide 21: Token Ring
IEEE 802.5
Flow is unidirectional
Each node regenerates signal (acts as repeater)
Control passed from interface to interface by “token”
Only one node at a time can have token
4 or 16 Mbps

## Slide 22: Fiber Distributed Data Interface (FDDI)
Dual counter rotating rings
  Devices can attach to one or both rings
  Single attachment station (SAS), dual (DAS)
Uses token passing
Logically and physically a ring
ANSI governed

## Slide 23: WANs
WANs connect LANs
Generally a single data link
Links most often come from Regional Bell Operating Companies (RBOCs) or Post, Telephone, and Telegraph (PTT) agencies
Wan link contains Data Terminal Equipment (DTE) on user side and Data Circuit-Terminating Equipment (DCE) at WAN provider’s end
MAN - Metropolitan Area Network

## Slide 24: OSI Model Revisited
Physical
Data Link
Network
Transport
Session
Presentation
Application

## Slide 25: Physical Layer
Specifies the electrical, mechanical, procedural, and functional requirements for activating, maintaining, and deactivating the physical link between end systems
Examples of physical link characteristics include voltage levels, data rates, maximum transmission distances, and physical connectors

## Slide 26: Physical Layer Hardware
Cabling
  twisted pair
  10baseT
  10base2
  10base5
  fiber
transceivers
hubs
topology

## Slide 27: Twisted Pair
10BaseT (10 Mbps, 100 meters w/o repeater)
Unshielded and shielded twisted pair (UTP most common)
two wires per pair, twisted in spiral
Typically 1 to 10 Mbps, up to 100Mbps possible
Noise immunity and emanations improved by shielding

## Slide 28: Coaxial Cable
10Base2 (10 Mbps, repeater every 200 m)
ThinEthernet or Thinnet or Coax
2-50 Mbps
Needs repeaters every 200-500 meters
Terminator: 50 ohms for ethernet, 75 for TV
Flexible and rigid available, flexible most common
Noise immunity and emanations very good

## Slide 29: Coaxial Cables, cont
Ethernet uses “T” connectors and 50 ohm terminators
Every segment must have exactly 2 terminators
Segments may be linked using repeaters, hubs

## Slide 30: Standard Ethernet
10Base5
Max of 100 taps per segment
Nonintrusive taps available (vampire tap)
Uses AUI (Attachment Unit Interface)

## Slide 31: Fiber-Optic Cable
Consists of Outer jacket, cladding of glass, and core of glass
fast

## Slide 32: Transceivers
Physical devices to allow you to connect different transmission media
May include Signal Quality Error (SQE) or “heartbeat” to test collision detection mechanism on each transmission
May include “link light”, lit when connection exists

## Slide 33: Hubs
A device which connects several other devices
Also called concentrator, repeater, or multi-station access unit (MAU)

## Slide 34: OSI Model Revisited
Physical
Data Link
Network
Transport
Session
Presentation
Application

## Slide 35: Data Link Layer
Provides data transport across a physical link
Data Link layer handles physical addressing, network topology, line discipline, error notification, orderly delivery of frames, and optional flow control
Bridges operate at this layer

## Slide 36: Data Link Sublayers
Media Access Control (MAC)
  refers downward to lower layer hardware functions
Logical Link Control (LLC)
  refers upward to higher layer software functions

## Slide 37: Medium Access Control (Data Link Sublayer)
MAC address is “physical address”, unique for LAN interface card
  Also called hardware or link-layer address
The MAC address is burned into the Read Only Memory (ROM)
MAC address is 48 bit address in 12 hexadecimal digits
  1st six identify vendor, provided by IEEE
  2nd six unique, provided by vendor

## Slide 38: Logical Link Control (Data Link Sublayer)
Presents a uniform interface to upper layers
Enables upper layers to gain independence over LAN media access
  upper layers use network addresses rather than MAC addresses
Provide optional connection, flow control, and sequencing services

## Slide 39: Bridges (Data Link Layer)
Device which forwards frames between data link layers associated with two separate cables
Stores source and destination addresses in table
When bridge receives a frame it attempts to find the destination address in its table
  If found, frame is forwarded out appropriate port
  If not found, frame is flooded on all other ports

## Slide 40: Bridges (Data Link Layer)
Can be used for filtering
  Make decisions based on source and destination address, type, or combination thereof
Filtering done for security or network management reasons
  Limit bandwidth hogs
  Prevent sensitive data from leaving
Bridges can be for local or remote networks
  Remote has “half” at each end of WAN link

## Slide 41: Network Layer
Which path should traffic take through networks?
How do the packets know where to go?
What are protocols?
What is the difference between routed and routing protocols?

## Slide 42: Network Layer
Name - what something is
  example is SSN
Address - where something is
Route - how to get there
  Depends on source

## Slide 43: Network Layer
Only two devices which are directly connected by the same “wire” can exchange data directly
Devices not on the same network must communicate via intermediate system
Router is an intermediate system
The network layer determines the best way to transfer data. It manages device addressing and tracks the location of devices. The router operates at this layer.

## Slide 44: Network Layer Bridge vs. Router
Bridges can only extend a single network
  All devices appear to be on same “wire”
  Network has finite size, dependent on topology, protocols used
Routers can connect bridged subnetworks
Routed network has no limit on size
  Internet, SIPRNET

## Slide 45: Network Layer
Provides routing and relaying
  Routing: determining the path between two end systems
  Relaying: moving data along that path
Addressing mechanism is required
Flow control may be required
Must handle specific features of subnetwork
  Mapping between data link layer and network layer addresses

## Slide 46: Connection-Oriented vs. Connectionless Network Layer
Connection-Oriented
  provides a Virtual Circuit (VC) between two end systems (like a telephone)
  3 phases - call setup, data exchange, call close
  Examples include X.25, OSI CONP, IBM SNA
  Ideal for traditional terminal-host networks of finite size

## Slide 47: Connection-Oriented vs. Connectionless Network Layer
Connectionless (CL)
  Each piece of data independently routed
  Sometimes called “datagram” networking
  Each piece of data must carry all addressing and routing info
  Basis of many current LAN/WAN operations
    TCP/IP, OSI CLNP, IPX/SPX
  Well suited to client/server and other distributed system networks

## Slide 48: Connection-Oriented vs. Connectionless Network Layer
Arguments can be made Connection Oriented is best for many applications
Market has decided on CL networking
  All mainstream developments on CL
  Majority of networks now built CL
  Easier to extend LAN based networks using CL WANs
We will focus on CL

## Slide 49: Network switching
Circuit-switched
  Transparent path between devices
  Dedicated circuit
    Phone call
Packet-switched
  Data is segmented, buffered, & recombined

## Slide 50: Network Layer Addressing
Impossible to use MAC addresses
Hierarchical scheme makes much more sense (Think postal - city, state, country)
This means routers only need to know regions (domains), not individual computers
The network address identifies the network and the host

## Slide 51: Network Layer Addressing
Network Address - path part used by router
Host Address - specific port or device
Router
1.1
1.2
1.3
2.1
2.2
2.3
Network
Host
1
2
1,2,3
1,2,3

## Slide 52: Network Layer Addressing IP example
IP addresses are like street addresses for computers
Networks are hierarchically divided into subnets called domains
Domains are assigned IP addresses and names
  Domains are represented by the network portion of the address
IP addresses and Domains are issued by InterNIC (cooperative activity between the National Science Foundation, Network Solutions, Inc. and AT&T)

## Slide 53: Network Layer Addressing IP
IP uses a 4 octet (32 bit) network address
The network and host portions of the address can vary in size
Normally, the network is assigned a class according to the size of the network
  Class A uses 1 octet for the network
  Class B uses 2 octets for the network
  Class C uses 3 octets for the network
  Class D is used for multicast addresses

## Slide 54
Class A Address
Used in an inter-network that has a few networks and a large number of hosts
First octet assigned, users designate the other 3 octets (24 bits)
Up to 128 Class A Domains
Up to 16,777,216 hosts per domain
0-127
This Field is
Fixed by IAB
24 Bits of
Variable Address
0-255
0-255
0-255

## Slide 55
Class B Address
Used for a number of networks having a number of hosts
First 2 octets assigned, user designates the other 2 octets (16 bits)
16384 Class B Domains
Up to 65536 hosts per domain
128-191
0-255
These Fields are
Fixed by IAB
16 Bits of
Variable Address
0-255
0-255

## Slide 56
Class C Address
Used for networks having a small amount of hosts
First 3 octets assigned, user designates last octet (8 bits)
Up to 2,097,152 Class C Domains
Up to 256 hosts per domain
191-223
0-255
0-255
These Fields are
Fixed by IAB
8 Bits of
Variable Address
0-255

## Slide 57: IP Addresses
A host address of all ones is a broadcast
A host address of zero means the wire itself
These host addresses are always reserved and can never be used

## Slide 58
Subnets & Subnet Masks
Every host on a network (i.e. same cable segment) must be configured with the same subnet ID.
  First octet on class A addresses
  First & second octet on class B addresses
  First, second, & third octet on class C addresses
A Subnet Mask (Netmask) is a bit pattern that defines which portion of the 32 bits represents a subnet address.
Network devices use subnet masks to identify which part of the address is network and which part is host

## Slide 59: Network Layer Routed vs. Routing Protocols
Routed Protocol - any protocol which provides enough information in its network layer address to allow the packet to reach its destination
Routing Protocol - any protocol used by routers to share routing information

## Slide 60: Routed Protocols
IP
IPX
SMB
Appletalk
DEC/LAT

## Slide 61
OSI Reference Model Protocol Mapping
6
5
4
3
2
1
7
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application using TCP/IP
TCP
IP
TCP/IP
UDP/IP
SPX/IPX
Application using UDP/IP
UDP
IP
Application using SPX/IPX
SPX
IPX

## Slide 62
Network-level Protocols
IPX (Internet Packet Exchange protocol)
  Novell Netware & others
  Works with the Session-layer protocol SPX (Sequential Packet Exchange Protocol)
NETBEUI (NetBIOS Extended User Interface)
  Windows for Workgroups & Windows NT
IP (Internet Protocol)
  Win NT, Win 95, Unix, etc…
  Works with the Transport-layer protocols TCP (Transmission Control Protocol) and UDP (User Datagram Protocol)
SLIP (Serial-line Input Protocol) & PPP (Point-to-Point Protocol)

## Slide 63
TCP/IP
Consists of a suite of protocols (TCP & IP)
Handles data in the form of packets
Keeps track of packets which can be
  Out of order
  Damaged
  Lost
Provides universal connectivity
  reliable full duplex stream delivery (as opposed to the unreliable UDP/IP protocol suite used by such applications as PING and DNS)

## Slide 64
TCP/IP (cont')
Primary Services (applications) using TCP/IP
  File Transfer (FTP)
  Remote Login (Telnet)
  Electronic Mail (SMTP)
Currently the most widely used protocol (especially on the Internet)
Uses the IP address scheme

## Slide 65: Routing Protocols
Vector-distancing
  List of destination networks with direction and distance in hops
Link-state routing
  Topology map of network identifies all routers and subnetworks
  Route is determined from shortest path to destination
Routes can be manually loaded (static) or dynamically maintained

## Slide 66: Routing Internet Management Domains
Core of Internet uses Gateway-Gateway Protocol (GGP) to exchange data between routers
Exterior Gateway Protocol (EGP) is used to exchange routing data with core and other autonomous systems
Interior Gateway Protocol (IGP) is used within autonomous systems

## Slide 67: Routing Internet Management Domains
GGP
IGP
IGP
EGP
EGP
Internet Core
Autonomous systems

## Slide 68: Routing Protocols
Static routes
  not a protocol
  entered by hand
  define a path to a network or subnet
  Most secure

## Slide 69: Routing Protocols RIP
Distance Vector
Interior Gateway Protocol
Noisy, not the most efficient
  Broadcast routes every 30 seconds
  Lowest cost route always best
  A cost of 16 is unreachable
No security, anyone can pretend to be a router

## Slide 70: Routing Protocols OSPF
Link-state
Interior Gateway Protocol
Routers elect “Designated Router”
All routers establish a topology database using DR as gateway between areas
Along with IGRP, a replacement for outdated RIP

## Slide 71: Routing Protocols BGP
Border Gateway Protocol is an EGP
Can support multiple paths between autonomous systems
Can detect and suppress routing loops
Lacks security
Internet recently down because of incorrectly configured BGP on ISP router

## Slide 72: Source Routing
Source (packet sender) can specify route a packet will traverse the network
Two types, strict and loose
Allows IP spoofing attacks
Rarely allowed across Internet

## Slide 73: Transport Layer
TCP
UDP
IPX Service Advertising Protocol
Are UDP and TCP connectionless or connection oriented?
What is IP?
Explain the difference

## Slide 74: Session Layer
Establishes, manages and terminates sessions between applications
  coordinates service requests and responses that occur when applications communicate between different hosts
Examples include: NFS, RPC, X Window System, AppleTalk Session Protocol

## Slide 75: Presentation Layer
Provides code formatting and conversion
For example, translates between differing text and data character representations such as EBCDIC and ASCII
Also includes data encryption
Layer 6 standards include JPEG, GIF, MPEG, MIDI

## Slide 76
Application-level Protocols
FTP (File Transfer Protocol)
TFTP (Trivial File Transfer Protocol)
  Used by some X-Terminal systems
HTTP (HyperText Transfer Protocol)
SNMP (Simple Network Management Protocol
  Helps network managers locate and correct problems in a TCP/IP network
  Used to gain information from network devices such as count of packets received and routing tables
SMTP (Simple Mail Transfer Protocol)
  Used by many email applications

## Slide 77: Identification & Authentication
Identify who is connecting - userid
Authenticate who is connecting
  password (static) - something you know
  token (SecureID) - something you have
  biometric - something you are
  RADIUS, TACACS, PAP, CHAP

## Slide 78: Firewall Terms
Network address translation (NAT)
  Internal addresses unreachable from external network
DMZ - De-Militarized Zone
  Hosts that are directly reachable from untrusted networks
ACL - Access Control List
  can be router or firewall term

## Slide 79: Firewall Terms
Choke, Choke router
  A router with packet filtering rules (ACLs) enabled
Gate, Bastion host, Dual Homed Host
  A server that provides packet filtering and/or proxy services
proxy server
  A server that provides application proxies

## Slide 80: Firewall types
Packet-filtering router
  Most common
  Uses Access Control Lists (ACL)
    Port
    Source/destination address
Screened host
  Packet-filtering and Bastion host
  Application layer proxies
Screened subnet (DMZ)
  2 packet filtering routers and bastion host(s)
  Most secure

## Slide 81: Firewall mechanisms
Proxy servers
  Intermediary
  Think of bank teller
Stateful Inspection
  State and context analyzed on every packet in connection

## Slide 82: Intrusion Detection (IDS)
Host or network based
Context and content monitoring
Positioned at network boundaries
Basically a sniffer with the capability to detect traffic patterns known as attack signatures

## Slide 83: Web Security
Secure sockets Layer (SSL)
  Transport layer security (TCP based)
  Widely used for web based applications
  by convention, https:\\
Secure Hypertext Transfer Protocol (S-HTTP)
  Less popular than SSL
  Used for individual messages rather than sessions
Secure Electronic Transactions (SET)
  PKI
  Financial data
  Supported by VISA, MasterCard, Microsoft, Netscape

## Slide 84: IPSEC
IP Security
  Set of protocols developed by IETF
  Standard used to implement VPNs
  Two modes
  Transport Mode
    encrypted payload (data), clear text header
  Tunnel Mode
    encrypted payload and header
  IPSEC requires shared public key

## Slide 85: Common Attacks
This section covers common hacker attacks
No need to understand them completely, need to be able to recognize the name and basic premise

## Slide 86: Spoofing
TCP Sequence number prediction
UDP - trivial to spoof (CL)
DNS - spoof/manipulate IP/hostname pairings
Source Routing

## Slide 87: Sniffing
Passive attack
Monitor the “wire” for all traffic - most effective in shared media networks
Sniffers used to be “hardware”, now are a standard software tool

## Slide 88: Session Hijacking
Uses sniffer to detect sessions, get pertinent session info (sequence numbers, IP addresses)
Actively injects packets, spoofing the client side of the connection, taking over session with server
Bypasses I&A controls
Encryption is a countermeasure, stateful inspection can be a countermeasure

## Slide 89: IP Fragmentation
Use fragmentation options in the IP header to force data in the packet to be overwritten upon reassembly
Used to circumvent packet filters

## Slide 90: IDS Attacks
Insertion Attacks
  Insert information to confuse pattern matching
Evasion Attacks
  Trick the IDS into not detecting traffic
  Example - Send a TCP RST with a TTL setting such that the packet expires prior to reaching its destination

## Slide 91: Syn Floods
Remember the TCP handshake?
  Syn, Syn-Ack, Ack
Send a lot of Syns
Don’t send Acks
Victim has a lot of open connections, can’t accept any more incoming connections
Denial of Service

## Slide 92: Telecom/Remote Access Security
Dial up lines are favorite hacker target
  War dialing
  social engineering
PBX is a favorite phreaker target
  blue box, gold box, etc.
  Voice mail

## Slide 93: Remote Access Security
SLIP - Serial Line Internet Protocol
PPP - Point to Point Protocol
  SLIP/PPP about the same, PPP adds error checking, SLIP obsolete
PAP - Password authentication protocol
  clear text password
CHAP - Challenge Handshake Auth. Prot.
  Encrypted password

## Slide 94: Remote Access Security
TACACS, TACACS+
  Terminal Access Controller Access Control System
  Network devices query TACACS server to verify passwords
  “+” adds ability for two-factor (dynamic) passwords
Radius
  Remote Auth. Dial-In User Service

## Slide 95: Virtual Private Networks
PPTP - Point to Point Tunneling Protocol
  Microsoft standard
  creates VPN for dial-up users to access intranet
SSH - Secure Shell
  allows encrypted sessions, file transfers
  can be used as a VPN

## Slide 96: RAID
Redundant Array of Inexpensive(or Independent) Disks - 7 levels
  Level 0 - Data striping (spreads blocks of each file across multiple disks)
  Level 1 - Provides disk mirroring
  Level 3 - Same as 0, but adds a disk for error correction
  Level 5 - Data striping at byte level, error correction too